## Slide 1: TCP and OSI model
Gulam Khan

## Slide 2: Encapsulation
Is the inclusion within a program object of all the resources need for the object to function.

## Slide 3: Decapsulation
Is the process of opening up encapsulated data that are usually sent in the form of packets over a communication network.

## Slide 4: TCP Layers
TCP has 4 Layers
  Process/Application Layer
  Host-to-Host Layer
  Internet Layer
  Network Layer

## Slide 5: TCP model
Process Application Layer
Performs the functions of the top three layers of the OSI model.
Host-to-Host Layer
Corresponds to the Transport Layer, responsible for end-to-end communication and error-free delivery of data.
Internet Layer
Analogous to Network Layer.
Network Access Layer
Responsible for node to node communication and controls user interface specifications
This layer corresponds to a combination of the data link layer and the physical layer of the OSI model.
Checks for hardware addressing (MAC address) and protocols present in this layer and allows for physical transmission of data (cables).
Broken up into three pieces
IP: Responsible for delivering packets from the source host to destination host by look at IP addresses in the packet headers.
ICMP: Encapsulated within IP datagram(packet) and is responsible for providing the host with information about issues with the network.
ARP: (Address Resolution Protocol) job is to find the hardware address of a host from a known IP address (IP  MAC).
Two main protocol at this layer are:
TCP (Transmission Control Protocol)
UDP (User Datagram Protocol)

## Slide 6: TCP Model VS OSI model
Process/Application Layer
Application Layer
Presentation Layer
Host-to-Host Layer
Transports Layer
Internet Layer
Network Layer
Network Access Layer
Session Layer
Data Link Layer
Physical Layer

## Slide 7: OSI Layers
OSI has seven Layers
  Application Layer
  Presentation Layer
  Session Layer
  Transport Layer
  Network Layer
  Data Link Layer
  Physical Layer

## Slide 8: OSI Model
Layer 1: Physical layer (The physics of the network)
Layer 2: Data link layer (The basic network language)
Layer 3: Network layer (Routing layer, Internet protocol)
Layer 4: Transport layer (TCP & UDP)
Layer 5: Session Layer (Communication management
Layer 6: Presentation Layer (Character coding, Application encryption)
Layer 7: Application Layer (The layer we see)

## Slide 9: Encryption
In computing, encryption is the method by which plain text or any other type of data is converted from a readable form to an encoded version.
It can only be decoded by another entity if they have access to a decryption key.
Encryption is one of the most important methods for providing data security, especially for end-to-end protection of data transmitted across networks.